## Slide 1: MICROCONTROLLERS
Microcontroller (MCU)
  Integrated electronic computing device that includes three major components on a single chip
    Microprocessor (MPU)
    Memory
    I/O (Input/Output) ports
Embedded systems use microcontrollers

## Slide 2: MICROPROCESSORS VS. MICROCONTROLLERS
MICROPROCESSOR | MICROCONTROLLER
CPU is stand-alone, RAM, ROM, I/O, timer are separate | CPU, RAM, ROM, I/O and timer are all on a single chip
designer can decide on the amount of ROM, RAM and I/O ports. | fixed amount of on-chip ROM, RAM, I/O ports
expensive | for applications in which cost, power and space are critical
versatility | single-purpose (control-oriented)
general-purpose | Low processing power
High processing power | Low power consumption
High power consumption | Bit-level operations
Instruction sets focus on processing-intensive operations | Instruction sets focus on control and bit level operations
Typically 32/64 – bit | Typically 8/16 bit
Typically deep pipeline (5-20 stages) | Typically single-cycle/two-stage pipeline

## Slide 3: BLOCK DIAGRAM OF MICROCONTROLLER
Support Devices
  Timers
  A/D converter
  Serial I/O
Common communication lines
  System Bus

## Slide 4: DIGITAL NUMBER SYSTEM
Microprocessors use binary number system
System | Base | Symbols
Decimal | 10 | 0, 1, … 9
Binary | 2 | 0, 1
Octal | 8 | 0, 1, … 7
Hexadecimal | 16 | 0, 1, … 9, A, B, … F

## Slide 5: COMPUTER LANGUAGES
1ST generation language
  binary (0 and 1) or machine level language
  Microprocessor can understand only the binary codes
2ND generation language
  Assembly level language
  Symbols
  Need to be converter to machine level language
3RD generation language
  High level language
  Use words and commands
  C,C++,Java
4TH generation language- close to human language

## Slide 6: COMPUTER LANGUAGES (cont.)
ASSEMBLER
COMPILER/ INTERPRETER
ASSEMBLY LEVEL LANGUAGE
HIGH LEVEL LANGUAGE
MACHINE LEVEL LANGUAGE
MACHINE LEVEL LANGUAGE

## Slide 7: Arduino UNO

## Slide 8: INTRODUCTION TO ARDUINO
A programmable micro controller for prototyping electromechanical devices
Can connect Digital and Analog electronic signals:
  Sensors (Gyroscopes, GPS Locators, accelerometers)
  Actuators (LEDS or electrical motors)

## Slide 9: HARDWARE ARCHITECTURE

## Slide 10: CONNECTION
USB A TO B

## Slide 11: SPECIFICATIONS OF ARDUINO
Microcontroller | ATmega328P
Operating Voltage | 5V
Input Voltage (recommended) | 7-12V
Input Voltage (limit) | 6-20V
Digital I/O Pins | 14 (of which 6 provide PWM output)
PWM Digital I/O Pins | 6
Analog Input Pins | 6
DC Current per I/O Pin | 20 mA
DC Current for 3.3V Pin | 50 mA
Flash Memory | 32 KB (ATmega328P) of which 0.5 KB used by bootloader
SRAM | 2 KB (ATmega328P)
EEPROM | 1 KB (ATmega328P)
Clock Speed | 16 MHz
Length | 68.6 mm
Width | 53.4 mm
Weight | 25 g