## Slide 1: Arduino ADC

## Slide 2: ADC
Translate analog voltage value into different digital levels
Analog Sensor output is connected to analog input pins.
6 analog pins A0 to A5

## Slide 3: Analog to Digital Conversion
Arduino has inbuilt 10 Bit ADC- 1024 discrete analog values.
  0 for 0V
  1023 for 5V
Example-Temperature sensor
  Sensor output range 0 to 100 °C
  0 °C corresponds to digital value 0
  100 °C corresponds to digital value 1023
  What will be the value corresponding to 50 °C??

## Slide 4: analogRead()
Reading analog value
  int x = analogRead(A3);
  // Reads the analog value on pin A3 into x

## Slide 5: LM35 - Temperature Sensor
Accurate than thermistor
Caliberated to an accuracy of 1 °C
Measurement range from -55 °C to 150 °C
1 °C corresponds to 10mV
Advantages
  Low cost
  Low supply current
  Low output impedance

## Slide 6: lm35 Pins

## Slide 7: TASKS
Write a program to turn on led when the temperature is greater than or equal to 35 degree Celsius.
Write a program to control the speed of a fan according to temperature.